## Slide 1
Partnering in growth, connecting people and supporting potential
DLNG PASSAGE INFORMATION OUTWARDS
PIL-PP-15
MASTER:_________________________________ SIGNATURE:___________________________
PILOT:___________________________________ SIGNATURE:___________________________
THE PRINCIPLES OF BRIDGE RESOURCE MANAGEMENT MUST BE ADHERED TO AT ALL TIMES
Teamwork | Respect | Integrity | Honesty | Safety
NAME OF VESSEL: ___________________________________ DATE: _____________________
POB TIME: ____________________ GT:__________________ DRAUGHT F: _______________
BERTH : ______________________ LOA:_________________ DRAUGHT A: _______________
STARBOARD SIDE ALONGSIDE – Refer to latest NTM for Declared Depths

## Slide 2
Partnering in growth, connecting people and supporting potential
Teamwork | Respect | Integrity | Honesty | Safety
DLNG PASSAGE INFORMATION OUTWARDS
PIL-PP-15
PLEASE NOTE:
* THE CHARTS USED ON THIS PASSAGE PLAN ARE NOT TO SCALE. THESE CHARTS FORM PART OF THE MASTER/PILOT EXCHANGE AND ARE FOR INFORMATION ONLY. NAVIGATIONAL CHARTS AND/OR APPROVED ECDIS SHOULD BE REFERRED TO IN ALL CASES.
* INDICATED COURSES ARE A GUIDELINE ONLY. VESSEL'S ROUTE IS TO BE DISCUSSED DURING THE MASTER/PILOT EXCHANGE AND AGREED TO BY THE MASTER.
* THE SHIP'S POSITION, THE VESSEL'S CONDITION AND HARBOUR TRAFFIC ARE TO BE MONITORED THROUGHOUT THE PASSAGE BY THE BRIDGE TEAM.
* THE BRIDGE TEAM MUST IMMEDIATELY MAKE THE PILOT AWARE OF ANY CONCERNS OR ANYTHING NOT UNDERSTOOD
BRIDGE TEAM:
MAINTAIN LOOKOUT VISUALLY AND BY RADAR. FOLLOW PILOT PASSAGE PLAN AND INFORM WHEN THERE IS AN OBSERVED DEVIATION FROM THE AGREED PLAN.
*IF IN DOUBT CONSULT PILOT*
MOORING LINES FOR DEPARTURE:
LET GO AND RECOVER ALL LINES IN ORDER.
ONLY SLACK AND LET GO LINES WHEN TOLD TO DO SO BY THE PILOT.
HEAD AND STERN LINES FIRST, THEN BREASTS, THEN SPRINGS LAST.
MOORING HOOKS: SWL 125t
MOORING HOOK ALARMS SET TO 40t
TUG INFORMATION:
SVITZER STOCKTON & MACQUARIE: ASD 82T
SVITZER PALMERSTON & STOKES: ASD 83T
MATARANKA: ASD 70T
FIONA
BERTHING LIMITS
Wind: 20kts (unless SE'ly then 25kts)
Tide: 3kts
DEPTHS:
As per latest NTM: Declared Depths
Critical Depth
Critical Depth
12.1m

## Slide 3
Partnering in growth, connecting people and supporting potential
DLNG PASSAGE INFORMATION OUTWARDS
PIL-PP-15
Teamwork | Respect | Integrity | Honesty | Safety
DARWIN PILOT PASSAGE PLAN
Route: DLNG to Outer Pilot Boarding Ground
OUTWARD BOUND
TOTAL DIST 14.8nm
Waypoint Name | LAT | LONG | Course x Distance to next Waypoint | Total Distance to Waypoint | Comments
DLNG Berth | 12o 31.434’ S | 130o 50.913’ E | 318o x 0.8nm |  | 
MA4 Buoy | 12o 30.819’ S | 130o 50.346’ E | 325o x 1.6nm | 0.8nm | Pass 0.18nm off MA4 Buoy
MA2 Buoy | 12o 29.483’ S | 130o 49.388’ E | 335o x 1.0nm | 2.4nm | Pass 0.13nm off MA2 Buoy
No.11 Buoy | 12o 28.585’ S | 130o 48.959’ E | 345o x 0.7nm | 3.4nm | Pass 0.10nm off No.11 Buoy
Elliott Point | 12o 27.943’ S | 130o 48.783’ E | 323o x 8.6nm | 4.1nm | Pass 0.45nm off Elliott Point
3 & 4 Buoys | 12o 21.108’ S | 130o 43.518’ E | 317o x 2.1nm | 12.7nm | Pass 1.35nm off Mandorah Jetty
OPBG | 12o 19.561’ S | 130o 42.042’ E |  | 14.8nm |