## Slide 1
Partnering in growth, connecting people and supporting potential
INPEX ILNG & ILPG PASSAGE INFORMATION INWARDS
PIL-PP-18
MASTER:_________________________________ SIGNATURE:___________________________
PILOT:___________________________________ SIGNATURE:___________________________
THE PRINCIPLES OF BRIDGE RESOURCE MANAGEMENT MUST BE ADHERED TO AT ALL TIMES
Teamwork | Respect | Integrity | Honesty | Safety
NAME OF VESSEL: ___________________________________ DATE: _____________________
POB TIME: ____________________ GT:__________________ DRAUGHT F: _______________
BERTH : ILPG/ILNG LOA:_________________ DRAUGHT A: _______________
PORTSIDE ALONGSIDE – Refer to latest NTM for Declared Depths
ILPG Berth & Tugs
Ch 87
Berthing Parameters
Wind 20kts except from SE <25kts
**Min. depth at berth to comply with
minimum UKC 1.5m until all fast**

## Slide 2
Partnering in growth, connecting people and supporting potential
Teamwork | Respect | Integrity | Honesty | Safety
INPEX ILNG & ILPG PASSAGE INFORMATION INWARDS
PIL-PP-18
PLEASE NOTE:
* THE CHARTS USED ON THIS PASSAGE PLAN ARE NOT TO SCALE. THESE CHARTS FORM PART OF THE MASTER/PILOT EXCHANGE AND ARE FOR INFORMATION ONLY. NAVIGATIONAL CHARTS AND/OR APPROVED ECDIS SHOULD BE REFERRED TO IN ALL CASES.
* INDICATED COURSES ARE A GUIDELINE ONLY. VESSEL'S ROUTE IS TO BE DISCUSSED DURING THE MASTER/PILOT EXCHANGE AND AGREED TO BY THE MASTER.
* THE SHIP'S POSITION, THE VESSEL'S CONDITION AND HARBOUR TRAFFIC ARE TO BE MONITORED THROUGHOUT THE PASSAGE BY THE BRIDGE TEAM.
* THE BRIDGE TEAM MUST IMMEDIATELY MAKE THE PILOT AWARE OF ANY CONCERNS OR ANYTHING NOT UNDERSTOOD
BRIDGE TEAM:
MAINTAIN LOOKOUT VISUALLY AND BY ALL AVAILABLE MEANS. FOLLOW PILOT PASSAGE PLAN & INFORM WHEN THERE IS AN OBSERVED DEVIATION FROM THE AGREED PLAN.
*IF IN DOUBT CONSULT PILOT*
MOORING LINES ON ARRIVAL:
ALL LINES ASHORE WITH HEAVING LINES AND YOYO GEAR. ONE LINE AT A TIME.
SPRINGS FIRST, THEN BREASTS, THEN HEAD/STERN LINES.
DON'T HEAVE UP UNTIL MOORING MEN ARE CLEAR OF MOORING DOLPHINS.
MOORING HOOKS: SWL 125t
MOORING HOOK ALARMS SET TO 40t
TUG INFORMATION:
STOCKTON & MACQUARIE: ASD 82T
PALMERSTON & STOKES: ASD 83T
MATARANKA: ASD 70T
Critical Depth

## Slide 3
Partnering in growth, connecting people and supporting potential
INPEX ILNG & ILPG INFORMATION INWARDS
PIL-PP-18
Teamwork | Respect | Integrity | Honesty | Safety